| Revision History: T-182T NAVIII and C-182T NAVIII GPU Instructions |
| --- |
| Date | Who | ID | Comments |
| Unknown | Thompson Valley Composite Squadron, Colorado Wing CAP | v1 | Initial revision |
| Unknown | 1st Lt Todd Gamber CAPID 443746 | v2 | Added more verbosity |
| 17 Mar 10 | 1st Lt Todd Gamber CAPID 443746 | v3 | Added revision history Changed the power-up check to look for 24 volts instead of negative amperage |
| 3 Mar 13 | Capt Todd Gamber CAPID 443746 | v4 | Added more specific text about what to do if the voltage drops below 24V when the GPU is connected. |

# T-182T NAVIII and C-182T NAVIII GPU Instructions

The Cessna T-182T uses a 28v power supply. The most common GPU is a red unit about the size of a mailbox with a 14/28v switch.

CAUTION: Engaging the autopilot should be avoided when the aircraft is not flying. Prolonged use can damage the servos and autopilot electronics.

Preparation

- Turn the GPU’s power switch “off”

- Be sure you have the voltage set to 28v when connecting it to a T-182T or a C-182T

- Plug the GPU power cord in to a standard 110v AC outlet

- Use a Phillips head driver to open the external power door on the pilot side of the cowling

- Plug the power harness into the aircraft’s external power plug. This plug is keyed; do not force the connector in if you are having trouble. This could be a sign it is connected incorrectly.

Power-up

- Ensure the aircraft avionics master switch set is off

- Ensure the aircraft STBY battery switch is off

- Ensure the aircraft battery/master switch set is off

- On the GPU, turn the power switch on.

- Turn on the aircraft battery/master switch

- Turn on the aircraft avionics master switches (buses 1 and 2)

- Verify PFD starts and volt meter is significantly above 24 volts (ideally ~27.5V)

  - NOTE: If the voltage decreases below 24V at any time while the GPU is connected, it means the GPU is not working properly, or not seated properly in the external power port. Perform the Shutdown checklist, and then the Preparation checklist before re-seating the external power plug.

Shutdown

- Turn off the aircraft avionics master switches (buses 1 and 2)

- Turn off the aircraft battery master switch

- Turn off the aircraft STBY battery switch

- Turn off the GPU

- Disconnect the GPU

- Close and fasten the aircraft external power door (cowling)

- Unplug the GPU