| Revision History: G1000 Observer Checklist, Civil Air Patrol, Jeffco Squadron |
| --- |
| Date | Who | ID | Revisions |
| 11 Dec 09 | 1st Lt Todd Gamber CAPID 443746 | v1 | Initial Revision. Included scenarios and time limits for each phase of the checklist. |
| 12 Mar 10 Next Revision Expected 12 Jul 10 | 1st Lt Todd Gamber CAPID 443746 | v2 | Changed to column layout and landscape orientation for kneeboard-like formatting. Moved all scenario-specific information to the “G1000 Instructor Checklist for Scenario-based Training” to make this checklist useful for real-world missions. Added footer Changed “En Route” segment to have 10 minute goal Changed preflight segment to have 10 minute goal |

# G1000 Observer Checklist

During preflight, during avionics fan test (if practical):

Goal: Perform these steps in 10 minutes or less.

- Delete all user waypoints and flight plans

- Enter search waypoint and/or user waypoint(s) for grid corner(s)

- Enter the first leg of the flight plan

- Store flight plan

- Ensure Becker DF is configured to listen to proper frequency

After engine startup, before taxi:

Goal: Perform these steps in 2 minutes or less.

- Configure audio panel for ATIS/AWOS and FM radio check

- Perform FM radio check

During taxi:

Goal: Perform these steps in 1 minutes or less.

- Load the saved flight plan and ensure first leg is activated

- Break the squelch to listen for static on 121.500MHz

Before takeoff:

Goal: Perform these steps in 30 seconds or less.

- Record time using the time on the MFD or PFD

- Ensure NAVIGATION MAP page is shown on the MFD

After take-off:

Goal: Perform these steps in 5 minutes or less.

- Reconfigure audio panel to report wheels up and listen to 121.500MHz

- Ensure the next leg of flight plan is entered

Enroute:

Goal: Perform these steps in 10 minutes or less.

- Ensure the search waypoint (or grid entry point) is in the active flight plan

- Ensure the active flight plan leg arrives at the search waypoint or grid entry point (use “Direct” if necessary)

- Switch to FM channel appropriate for the search area

- Ensure NAVIGATION MAP page is shown on MFD

In Grid:

- Perform search duties and assist with pilot workload

Exiting Grid:

- Enter and activate the return route in a flight plan

Return route:

- Switch to FM repeater channel appropriate for the area

After landing:

- Configure the audio panel to report wheels down, break the squelch on 121.500 MHz, and for ground communication